Solution for small porches or railings that prevent proper positioning of the PPA blower

Walter Cover

Parts:  Shower curtain compression bar

Heavy vinyl, about 3’ long and 40 “ wide

1” pipe about 40” long

Double the vinyl, sew around edges, sew in a loop at the top for the compression bar.  Sew a loop in the bottom for the pipe to slide into, sew the end to secure.

Used for those incidents where you have a small porch or porch rails that prevent positioning the blower the required distance.  Compress the top bar and fit into  the top of the door jamb, un-roll. The bar at the bottom is wider than the door thus preventing the cover from being blown into the building when the blower is started.  The blower can be positioned closer to the door, you only need to seal the bottom half of the door.